## Slide 1
FIT3143 • Applied 2 • Tasks 1 and 2
GPU image rotation
and responsible HPC for AI
CUDA design and performance • Evidence, trade-offs and accountable use
Savin Vindiv De Alwis · 35221631
sdea0018@student.monash.edu
Shamle Thilaksiri · 35512075
wthi0003@student.monash.edu
8 October 2026 • Detailed evidence, references and AI records follow in the appendix

## Slide 2
Task 1(a)
Host–GPU image data flow
CPU: load/decode, allocate, launch, save
GPU: read input, rotate, write output
Storage
encoded
image
Host RAM
DDR example
input pixels
GPU memory
GDDR / HBM
input buffer
GPU memory
GDDR / HBM
output buffer
Host RAM
output pixels
CPU
decode
H2D
PCIe
CUDA
kernel
D2H
PCIe
Separate host/device buffers; transfer engines perform DMA. PCIe link bandwidth differs from
bandwidth inside GPU memory.
Pinned RAM supports efficient transfers; pageable RAM may need staging. Wait for completed output
before host saving or buffer reuse.
The CPU orchestrates I/O and launches; the GPU rotates decoded pixels.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model; [5] NVIDIA CUDA Best Practices
2 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 3
Task 1(b)
Rotation as independent output work
Inverse mapping in y-down image coordinates
sx = c*(x-cx) - s*(y-cy) + cx;
sy = s*(x-cx) + c*(y-cy) + cy;
ix = floor(sx + 0.5);
iy = floor(sy + 0.5);
c = cos θ; s = sin θ; center = ((W−1)/2, (H−1)/2)
Output pixel
(x,y)
Nearest input
(ix,iy)
lookup
Positive θ rotates visually counterclockwise. Use a fixed canvas; rounded
source indices outside the image produce black.
Brightness touches the same pixel in/out; rotation gathers a different
source. Nearest-neighbour sampling is simple but can alias.
One thread owns one output pixel: gather a source value, then write once.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model
3 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html

## Slide 4
Task 1(b)
CUDA launch and execution hierarchy
dim3 block(16,16);
dim3 grid(64,64);
rotate_rgb<<<grid,block>>>(
d_in,d_out,1024,1024,c,s);
x = blockIdx.x*blockDim.x + threadIdx.x;
y = blockIdx.y*blockDim.y + threadIdx.y;
if (x >= W || y >= H) return;
1024 × 1024 output
64 × 64 = 4,096 blocks
16 × 16 = 256 threads/block
1,048,576 logical threads
32 threads/warp → 8 warps/block
One highlighted warp within a 16-wide block
Non-multiple dimensions: ceil-divide the grid and keep the bounds guard.
A grid specifies logical work; finite SMs schedule its blocks and warps.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model
4 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html

## Slide 5
Task 1(b)
CUDA features that affect throughput
Example: independent brightness channels
int p = 3*(y*W + x);
for (int ch=0; ch<3; ++ch) {
int v = int(in[p+ch]) + delta;
out[p+ch] = v<0 ? 0 : (v>255 ? 255 : v);
}
Excerpt after coordinate/bounds checks; wider offsets used in full code.
Pending blocks
Streaming multiprocessor
resident warps → execution units
SIMT: a warp issues common
instructions. Divergent paths can
reduce efficiency.
Resident warps hide latency; registers limit residency.
Coalescing groups nearby accesses into fewer transactions;
rotation can disrupt read locality.
Concurrency helps only when memory access and resource use support it.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model; [5] NVIDIA CUDA Best Practices
5 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 6
Task 1(b)
Expected speedup and its limits
Baseline: single CPU thread, same rotation and sampling
Also compare a multithreaded CPU; identical output and timing boundaries.
Speedup = TCPU / TGPU,total
TGPU,total = allocation/setup + H2D + kernel + D2H
Many GPU execution units and high device
bandwidth favor parallel throughput. Large or
resident images amortize setup; gathered reads
may limit bandwidth.
Week 7: S = 1 / (s + (1−s)/a). s is the unchanged
serial share; a accelerates the remainder. s = 0.20
gives a 5× ideal ceiling before added transfers.
Theoretical, not measured.
Expect gains for large or resident workloads; measure the whole pipeline.
Sources: [2] Topic 7A: dependencies and Amdahl; [5] NVIDIA CUDA Best Practices
6 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 7
Task 1(c)
GPUDirect Storage and rotation
Conventional storage path
Storage
Host staging RAM
GPU memory
storage read
H2D / PCIe
GDS direct path (supported configuration)
Storage-side DMA
NVMe / NIC
GPU memory
PCIe data path bypasses host staging
CPU issues cuFile I/O; compatibility fallback may stage through RAM.
CPU-decoded / already-in-RAM image: little benefit. Large storage-bound batches with GPU-ready data:
possible benefit, verify direct path and total time.
GDS can reduce storage staging; it does not accelerate rotation arithmetic.
Sources: [6] NVIDIA GDS overview; [7] NVIDIA GDS design
7 / 56
Notes: [6] NVIDIA, GPUDirect Storage Overview Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/overview-guide/index.html
[7] NVIDIA, GPUDirect Storage Design Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/design-guide/index.html

## Slide 8
Task 2 • HPC and AI
Parallel training across a compute cluster
GPU 0
same model
data partition A
GPU 1
same model
data partition B
GPU 2
same model
data partition C
Gradient all-reduce: average + share → consistent update on every GPU
Interconnect:
latency and bandwidth
Gradient synchronization
before each update
HPC combines processors, memory, networks and
storage. Tensor/pipeline parallelism can also split a
model.
More GPUs enable larger work; communication,
serial work and imbalance limit speedup. Evaluate
useful output against resource cost.
Scaling adds capacity and communication: ethical costs depend on useful work.
Sources: [2] Topic 7A: dependencies and Amdahl; [3] Topic 9A: synchronization; [8] NVIDIA Megatron parallelism; [21] Week 5: collective communication
8 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[8] NVIDIA, “Parallelism strategies guide,” Megatron Core, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/megatron-core/developer-guide/latest/user-guide/parallelism-guide.html
[21] Monash University, FIT3143 Week 5 combined course material, MPI collectives, pp. 148–155.
../context/FIT3143_Week_5_Combined.pdf

## Slide 9
Task 2(a)
Electricity demand and environmental costs
Global data-centre electricity (TWh/year)
Electricity growth during 2025
Chart: 
| 2025 estimate | 2030 projection
Electricity (TWh) | 485 | 950
Chart: 
| All data centres | AI-focused subset
2025 growth | 0.17 | 0.5
IEA 2026: ≈96% increase to 2030. These cover the whole sector, not AI training alone; growth categories overlap and
cannot be added.
Research comparison: Green AI [13] emphasizes efficiency; water research [12] adds site/time constraints. Track energy,
carbon and local cooling impacts.
Sources: [9] IEA 2026: sector estimates and projection; [12] Li et al. 2025 revision: water impacts; [13] Schwartz et al. 2019: efficiency reporting
9 / 56
Notes: [9] International Energy Agency, Key Questions on Energy and AI, executive summary, Apr. 16, 2026, CC BY 4.0, accessed Oct. 8, 2026.
https://www.iea.org/reports/key-questions-on-energy-and-ai/executive-summary
[12] P. Li, J. Yang, M. A. Islam, and S. Ren, “Making AI less ‘thirsty’: Uncovering and addressing the secret water footprint of AI models,” arXiv:2304.03271v5, Mar. 26, 2025; first submitted 2023.
https://arxiv.org/abs/2304.03271v5
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597

## Slide 10
Task 2(b)
Privacy, security and model fairness
Security: protect distributed intermediates
Fairness: evaluate affected groups
Workers exchange gradients
and save checkpoints
Least privilege, isolation,
protected transport/storage
Data coverage and model outputs
may differ across groups
Disaggregated, harm-specific tests
+ mitigation and reevaluation
Zhu et al. [14]: exposed gradients can reconstruct
inputs in studied settings. Not every production
collective leaks.
Gallegos et al. [15]: metrics, datasets and mitigations
differ. Apply these to cluster-trained models; scale alone
does not guarantee fairness.
Provenance/permissions, replica access and dual-use review need owners. Encryption alone cannot establish fair outputs.
Protect distributed data and evaluate harms; more compute is not a fairness guarantee.
Sources: [14] Zhu et al. 2019: exposed gradients; [15] Gallegos et al. 2024: fairness evaluation; [18] OECD: rights, fairness and accountability; [19] NIST: Govern, Map, Measure,
Manage
10 / 56
Notes: [14] L. Zhu, Z. Liu, and S. Han, “Deep leakage from gradients,” arXiv:1906.08935v2, 2019.
https://arxiv.org/abs/1906.08935v2
[15] I. O. Gallegos et al., “Bias and fairness in large language models: A survey,” Computational Linguistics, vol. 50, no. 3, pp. 1097–1179, 2024, doi: 10.1162/coli_a_00524.
https://aclanthology.org/2024.cl-3.8/
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 11
Task 2(c)
Unequal access to HPC resources
Evidence | What it shows | What it cannot establish
Ahmed & Wahed [16] | Historical research participation and compute concentration | Current worldwide access or a universal causal effect
Strubell et al. [11] | Selected NLP workload costs and financial barriers | The cost of every current AI workload
Current response: NAIRR supported >600 teams and >6,000 students
NSF, March 2026; US programme since 2024. Reach does not prove global equality.
Proposal: transparent GPU-hour allocation, smaller-institution support and appeals. Trade-off: reserved
access can reduce immediate utilization or delay urgent jobs.
Shared capacity helps; allocation, expertise and reproducibility still need support.
Sources: [10] NSF 2026: US programme reach; [11] Strubell et al. 2019: cost and equity; [16] Ahmed and Wahed 2020: compute divide
11 / 56
Notes: [10] U.S. National Science Foundation, “NAIRR at 2 years: Advancing American artificial intelligence innovation and leadership,” Mar. 19, 2026, accessed Oct. 8, 2026.
https://www.nsf.gov/cise/updates/nairr-2-years-advancing-american-artificial-intelligence
[11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL, 2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[16] N. Ahmed and M. Wahed, “The de-democratization of AI: Deep learning and the compute divide in artificial intelligence research,” arXiv:2010.15581v1, 2020.
https://arxiv.org/abs/2010.15581v1

## Slide 12
Task 2(d)
An accountable HPC approval process
Define outcome
+ accountable owner
Measure quality,
energy and harms
Approve / defer /
reduce scale / redesign
Green AI: efficiency evidence [13] • Carbon-aware scheduling: flexible work [17]
OECD: values and rights [18] • NIST: Govern, Map, Measure, Manage [19]
Use an energy budget, security/group evaluation and transparent access rules. Record owner, rationale,
exceptions and outcomes.
Measurement informs action: shift flexible jobs to cleaner periods within deadlines/capacity. Forecast
uncertainty, water stress and urgent access can change the decision.
Approve useful work with explicit budgets, safeguards and an accountable owner.
Sources: [13] Schwartz et al. 2019: efficiency reporting; [17] Radovanovic et al. 2021: flexible scheduling; [18] OECD: rights, fairness and accountability; [19] NIST: Govern, Map,
Measure, Manage
12 / 56
Notes: [13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 13
Appendix • Reading guide
Supporting detail and limitations
Task 1: design evidence
Rotation assumptions, a worked example and full
CUDA teaching excerpts are included on the
following slides.
Performance explanations use a stated CPU
baseline and theoretical bounds. No measured
speedup or compiled CUDA result is claimed.
GDS is evaluated for the actual CPU-decoded
pipeline and a conditional storage-bound batch
alternative.
Task 2: research and decisions
Each required topic has evidence, a comparison,
proposed measures and limitations. A cluster
scenario is illustrative, not an observed experiment.
Sector electricity data do not establish a particular
training job’s footprint. Historical research is
distinguished from current programme reach.
References and AI disclosure/prompt records are
part of this presentation. There is no separate report
dependency.
FIT3143 Applied 2
13 / 56

## Slide 14
Appendix A1
Rotation coordinates and sampling
Coordinate convention
Input/output: contiguous 8-bit RGB; positive width W
and height H; x points right and y points down. Input
and output buffers are distinct.
Rotate around cx = (W − 1)/2 and cy = (H − 1)/2.
Positive θ is visually counterclockwise; the host
supplies c = cos θ and s = sin θ in radians.
Forward image-coordinate rotation uses [c s; −s c].
Inverting it gives source offsets [c −s; s c] × output
offsets, then restores the center.
Deliberate design choices
Nearest-neighbour indices: ix = floor(sx + 0.5), iy =
floor(sy + 0.5). Copy three channels if the rounded
indices are in bounds; otherwise write black.
The fixed W × H canvas can crop rotated corners.
Nearest-neighbour sampling can alias; bilinear
interpolation improves smoothness but adds source
reads/arithmetic.
Forward scatter can leave holes or competing writes
after rounding. Inverse gathering assigns every
output exactly one writer. NPP offers library rotation
with explicit interpolation/ROI choices.
Sources: [1] Topic 8: GPU architecture and CUDA; [20] NVIDIA NPP: library alternative
14 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[20] NVIDIA, “Rotate,” NPP Image Geometry Transforms, CUDA 13.0.3 archive documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/archive/13.0.3/npp/image_geometry_transforms.html#rotate

## Slide 15
Appendix A2
A 90-degree rotation example
Input
0 | 1 | 2 | 3 | 4
5 | 6 | 7 | 8 | 9
10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24
Output: 90° counterclockwise
4 | 9 | 14 | 19 | 24
3 | 8 | 13 | 18 | 23
2 | 7 | 12 | 17 | 22
1 | 6 | 11 | 16 | 21
0 | 5 | 10 | 15 | 20
θ = 90°
c = 0, s = 1
center = (2,2)
Output (0,1) → source (3,0) → value 3
The matrix values are illustrative pixel identifiers, not channel intensities.
FIT3143 Applied 2
15 / 56

## Slide 16
Appendix A3
Crafted CUDA example: RGB brightness
__global__ void brightness_rgb(const unsigned char* input,
unsigned char* output,
int width,
int height,
int brightness) {
const int x = blockIdx.x * blockDim.x + threadIdx.x;
const int y = blockIdx.y * blockDim.y + threadIdx.y;
if (x >= width || y >= height) {
return;
}
const size_t offset = (size_t(y) * size_t(width) + size_t(x)) * 3;
for (int channel = 0; channel < 3; ++channel) {
const int value = int(input[offset + channel]) + brightness;
output[offset + channel] =
value < 0 ? 0 : (value > 255 ? 255 : value);
}
}
Same operation on
independent pixels: a
data-parallel kernel.
Integer arithmetic avoids
unsigned wrap; clamp each
channel to [0,255].
Adjacent threads touch
adjacent pixel locations,
providing useful locality.
Illustrative CUDA C++;
uncompiled and
unbenchmarked.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model
16 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html

## Slide 17
Appendix A4
Crafted CUDA example: inverse mapping
__global__ void rotate_rgb(const unsigned char* input,
unsigned char* output,
int width,
int height,
float c,
float s) {
const int x = blockIdx.x * blockDim.x + threadIdx.x;
const int y = blockIdx.y * blockDim.y + threadIdx.y;
if (x >= width || y >= height) {
return;
}
const float cx = (width - 1) * 0.5f;
const float cy = (height - 1) * 0.5f;
const float sx = c * (x - cx) - s * (y - cy) + cx;
const float sy = s * (x - cx) + c * (y - cy) + cy;
const int ix = int(floorf(sx + 0.5f));
const int iy = int(floorf(sy + 0.5f));
Global coordinates come from
block/thread indices.
The guard handles partial edge
blocks before any memory
access.
The host computes sine/cosine
once per angle.
Nearest-neighbour mapping
uses the documented y-down
convention.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model
17 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html

## Slide 18
Appendix A5
Crafted CUDA example: safe output writes
const size_t destination = (size_t(y) * size_t(width) + size_t(x)) * 3;
if (ix >= 0 && ix < width && iy >= 0 && iy < height) {
const size_t source = (size_t(iy) * size_t(width) + size_t(ix)) * 3;
for (int channel = 0; channel < 3; ++channel) {
output[destination + channel] = input[source + channel];
}
} else {
for (int channel = 0; channel < 3; ++channel) {
output[destination + channel] = 0;
}
}
}
RGB address = 3 × (row ×
width + column).
Every valid output gets three
channels, including black
borders.
No atomics, mutex or block
barrier is needed: writers have
disjoint destinations.
Total work Θ(W × H);
input/output storage Θ(W × H)
each.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model; [22] Topic 9B: mutual exclusion and allocation
18 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
[22] Monash University, FIT3143 Topic 9B: Mutual exclusion and resource allocation, course slides, 2024, pp. 4–16, 24–32.
../context/FIT3143-Topic-9B-2024.pdf

## Slide 19
Appendix A6
Host orchestration and completion
dim3 block(16, 16);
dim3 grid(1u + (unsigned(W)-1u)/block.x,
1u + (unsigned(H)-1u)/block.y);
cudaMemcpy(d_in, h_in, bytes,
cudaMemcpyHostToDevice);
rotate_rgb<<<grid, block>>>(
d_in, d_out, W, H, c, s);
cudaGetLastError();
cudaMemcpy(h_out, d_out, bytes,
cudaMemcpyDeviceToHost);
Illustrative excerpt, not a complete program: W/H > 0; bytes = 3 × W
× H checked in size_t; valid separate buffers; grid/device limits
validated.
CPU loads/decodes, allocates host/device
buffers, checks every API/launch/completion
result, saves output and frees resources
safely.
For this ordered synchronous-copy example,
D2H supplies completed host data. A launch is
asynchronous; launch-error checks alone do
not establish successful completion.
Pinned host storage is page-locked and
supports efficient DMA. Pageable memory
may need runtime staging. Avoid excessive
pinning.
Sources: [1] Topic 8: GPU architecture and CUDA; [3] Topic 9A: synchronization; [4] NVIDIA CUDA programming model; [5] NVIDIA CUDA Best Practices
19 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 20
Appendix A7
Launch shape and memory access
Choice | Mechanism | Performance implication
16 × 16 block | 256 threads; each warp spans two 16-wide rows | Reasonable 2D starting point; row edges/alignment matter.
32 × 8 block | 256 threads; each warp spans one 32-wide row | May improve row-oriented access; no universal winner.
Output gathering | Adjacent x threads write adjacent RGB pixels | Useful write locality; per-channel byte operations still require efficient transactions.
Rotated input reads | Angle changes the source addresses visited by a warp | Irregular gathers can reduce effective read bandwidth/cache reuse.
Higher residency | Registers, shared memory and block/thread limits constrain active warps | Helps hide latency; maximum occupancy is not automatically fastest.
Recompute grid for each block shape. Profile actual transactions, latency and registers before selecting a shape.
Sources: [1] Topic 8: GPU architecture and CUDA; [4] NVIDIA CUDA programming model; [5] NVIDIA CUDA Best Practices
20 / 56
Notes: [1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35, 41–46.
../context/FIT3143-Topic-8-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 21
Appendix A8
Asynchronous work within one stream
cudaError_t enqueue_rotation(const unsigned char* h_input,
unsigned char* h_output,
unsigned char* d_input,
unsigned char* d_output,
size_t bytes, int width, int height,
float c, float s, cudaStream_t stream) {
const dim3 block(32, 8); // Compare against dim3(16, 16) when profiling.
const dim3 grid = rotation_grid(width, height, block);
cudaError_t status = cudaMemcpyAsync(d_input, h_input, bytes,
cudaMemcpyHostToDevice, stream);
if (status != cudaSuccess) return status;
rotate_rgb<<<grid, block, 0, stream>>>(d_input, d_output,
width, height, c, s);
status = cudaGetLastError();
if (status != cudaSuccess) return status;
return cudaMemcpyAsync(h_output, d_output, bytes,
cudaMemcpyDeviceToHost, stream);
}
Full enqueue function from the
supplied performance
example.
Pinned host buffers and
checked sizes are
preconditions.
Success means submitted
work; wait before reading,
reusing or freeing buffers.
On error, previously enqueued
work may still be pending.
Sources: [3] Topic 9A: synchronization; [5] NVIDIA CUDA Best Practices
21 / 56
Notes: [3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 22
Appendix A9
Batch overlap and GPU residency
Same stream: H2D → kernel → D2H, in order
Stream A / image A
H2D
Kernel
D2H
Stream B / image B
H2D
Kernel
D2H
Schematic overlap opportunity; not measured durations or guaranteed simultaneous execution.
Independent streams + separate pinned/device buffers + supporting copy/compute resources. Synchronize
before reuse. Extra buffers consume memory; device residency avoids unnecessary round trips.
Overlap changes the critical path, not the amount of rotation work.
Sources: [3] Topic 9A: synchronization; [5] NVIDIA CUDA Best Practices
22 / 56
Notes: [3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 23
Appendix A10
Fair speedup comparison and profiling
Comparable baselines
Primary baseline: one CPU thread performs the
same RGB inverse mapping, nearest-neighbour rule
and fixed canvas. Also compare a multithreaded
CPU for a stronger practical baseline.
Use identical inputs/angles and verify identical or
justified numerically equivalent outputs. Include file
decoding/I/O in both paths or exclude it from both.
For the stated decoded-buffer comparison, include
GPU allocation, H2D, launch, completed kernel and
D2H; CPU timing covers the corresponding output
allocation and rotation.
Measure the bottleneck
Report cold-start and warmed repeated runs
separately. Use CUDA events for kernel elapsed
time after completion and a host timer through final
completion for total latency.
Vary image size, angle, block shape and batch size;
record hardware, transfer mode, register use and
effective memory/link bandwidth.
The sequential sum does not apply unchanged to
overlapping streams: measure the completed batch
critical path. Lower kernel time alone cannot
establish end-to-end speedup.
Sources: [2] Topic 7A: dependencies and Amdahl; [5] NVIDIA CUDA Best Practices
23 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html

## Slide 24
Appendix A11
GDS decision for the proposed pipeline
Conventional decoded-image path
CPU decoding requires host-visible compressed
bytes and produces pixels in RAM. Those pixels are
copied to the GPU; the rotation kernel then runs.
A single small image already in RAM gains little from
bypassing a storage step that is no longer on its
path.
GDS does not decode an image, bypass an
application’s CPU transformation, or make GPU
memory access itself faster.
Conditional batch alternative
Large storage-bound batches of GPU-ready pixels,
or a compatible GPU decoding pipeline, may avoid
host staging via cuFile and storage-side DMA.
Verify the GPU, storage/filesystem, software and
PCIe topology support the direct path. Compatibility
fallback uses host staging and is not evidence of
direct DMA.
Adopt only if completed batch time/CPU overhead
improve on the real workload; include extra buffers,
decoding and storage bandwidth. Otherwise retain
conventional copies.
Sources: [6] NVIDIA GDS overview; [7] NVIDIA GDS design
24 / 56
Notes: [6] NVIDIA, GPUDirect Storage Overview Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/overview-guide/index.html
[7] NVIDIA, GPUDirect Storage Design Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/design-guide/index.html

## Slide 25
Appendix B1
Parallelism, dependencies and scaling limits
Model | Partition and communication | Scaling limitation
Data parallel | Replicate model; partition batches; reduce/average gradients before a consistent update | Collective latency/bandwidth and stragglers.
Tensor parallel | Partition computations within a layer; exchange partial results | Frequent inter-device communication.
Pipeline parallel | Assign layers to stages; pass activations/gradients | Stage imbalance and pipeline bubbles.
Fixed workload | More GPUs reduce only the parallelizable portion | Serial work and communication bound speedup.
Larger workload | Scale capacity/model/data with added resources | A different claim from halving a fixed job’s runtime.
All-reduce is a collective result-sharing concept, not a claim that every AI framework uses the exact classroom MPI code.
Sources: [2] Topic 7A: dependencies and Amdahl; [3] Topic 9A: synchronization; [8] NVIDIA Megatron parallelism; [21] Week 5: collective communication
25 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[8] NVIDIA, “Parallelism strategies guide,” Megatron Core, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/megatron-core/developer-guide/latest/user-guide/parallelism-guide.html
[21] Monash University, FIT3143 Week 5 combined course material, MPI collectives, pp. 148–155.
../context/FIT3143_Week_5_Combined.pdf

## Slide 26
Appendix B2 • Illustrative calculation
A faster job can consume more energy
Assumed configuration | Completed runtime | Whole-job energy
Lower parallel scale; 1 kW | 2.0 hours | 1 × 2.0 = 2.0 kWh
Higher parallel scale; 2 kW | 1.2 hours | 2 × 1.2 = 2.4 kWh
Illustrative constant power assumptions, not measurements. Same useful output is assumed; faster completion uses 20%
more energy here.
E = ∫ P(t) dt • Carbon ≈ Σ Einterval × carbon intensity
Sources: [2] Topic 7A: dependencies and Amdahl; [11] Strubell et al. 2019: cost and equity; [13] Schwartz et al. 2019: efficiency reporting
26 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL, 2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597

## Slide 27
Appendix B3
Environmental accounting and evidence limits
Define what is counted
Energy (kWh) integrates power (kW) over hours.
Operational emissions ≈ Σ energy in each interval ×
that interval’s carbon intensity (kg CO₂e/kWh).
Report accelerators, host CPUs, storage/networking
and allocated cooling overhead; include failed runs
and repeated tuning when evaluating a project.
Hardware manufacture and disposal are embodied
impacts beyond operational electricity. Water
withdrawal and water consumption are different
measures.
Compare the evidence
Strubell et al. quantify costs for selected historical
NLP training/development workloads; those values
are not universal 2026 model footprints.
Green AI motivates reporting efficiency alongside
accuracy; Li et al. show why water varies with
place/time. Carbon alone misses local water
pressures.
IEA sector totals provide context, not causal
attribution to one model. Forecasts depend on
demand and infrastructure assumptions; local
grid/cooling effects differ by site.
Sources: [9] IEA 2026: sector estimates and projection; [11] Strubell et al. 2019: cost and equity; [12] Li et al. 2025 revision: water impacts; [13] Schwartz et al. 2019: efficiency
reporting
27 / 56
Notes: [9] International Energy Agency, Key Questions on Energy and AI, executive summary, Apr. 16, 2026, CC BY 4.0, accessed Oct. 8, 2026.
https://www.iea.org/reports/key-questions-on-energy-and-ai/executive-summary
[11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL, 2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[12] P. Li, J. Yang, M. A. Islam, and S. Ren, “Making AI less ‘thirsty’: Uncovering and addressing the secret water footprint of AI models,” arXiv:2304.03271v5, Mar. 26, 2025; first submitted 2023.
https://arxiv.org/abs/2304.03271v5
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597

## Slide 28
Appendix B4 • Proposed cluster policy
Governance controls and remaining risks
Risk / stakeholder | Proposed control | Residual limitation / owner
Dataset misuse / data subjects | Provenance, permission checks, retention limits and access logs | A licence alone may not justify every use; data steward reviews purpose.
Gradient/checkpoint exposure / participants | Least privilege, tenant isolation, protected transport and secure checkpoint storage | Authorized endpoints can still see sensitive values; security owner models insider risk.
Unsafe dual use / affected public | Authorized-use review, restricted access where justified and review of deployment risks | Controls cannot prevent every misuse; accountable owner weighs benefits/restrictions.
Distributed replicas / operators | Track copies, deletion obligations and incident response across workers | Replication increases the number of assets to protect; operator audits recovery.
These are proposed mitigations informed by research/frameworks, not a proof of privacy or a compliance certification.
Sources: [14] Zhu et al. 2019: exposed gradients; [18] OECD: rights, fairness and accountability; [19] NIST: Govern, Map, Measure, Manage
28 / 56
Notes: [14] L. Zhu, Z. Liu, and S. Han, “Deep leakage from gradients,” arXiv:1906.08935v2, 2019.
https://arxiv.org/abs/1906.08935v2
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 29
Appendix B5 • Proposed example
Fairness evaluation with large-scale compute
Compute connection
An illustrative multilingual AI service may have
unequal performance or stereotyped outputs across
language groups. Identify the actual harm before
choosing a metric.
A cluster enables larger datasets and repeated
training, but neither data volume nor GPU count
guarantees representative data or equitable
outcomes.
Reserve evaluation compute for affected groups;
document dataset coverage and compare
disaggregated error or harmful-output rates using a
task-appropriate test.
Evidence and decision
Gallegos et al. separate metrics, evaluation datasets
and mitigation stages. A single aggregate accuracy
score can hide a relevant subgroup harm.
Specify justified acceptance criteria before training;
examine uncertainty and small-group sample limits.
Mitigate, reevaluate, and document unresolved
harms.
Security and fairness have different objectives:
encrypted gradients do not establish fair outputs.
The source supports model-bias analysis, not a
claim that HPC itself causes bias.
Sources: [15] Gallegos et al. 2024: fairness evaluation; [18] OECD: rights, fairness and accountability; [19] NIST: Govern, Map, Measure, Manage
29 / 56
Notes: [15] I. O. Gallegos et al., “Bias and fairness in large language models: A survey,” Computational Linguistics, vol. 50, no. 3, pp. 1097–1179, 2024, doi: 10.1162/coli_a_00524.
https://aclanthology.org/2024.cl-3.8/
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 30
Appendix B6
Access research and allocation choices
Research comparison
Ahmed and Wahed study historical conference
participation and a compute divide. Strubell et al.
examine financial/resource barriers in selected NLP
workloads.
The first concerns institutional participation; the
second concerns workload cost. Together they
motivate access support, but neither is a current
worldwide access census.
NSF’s March 2026 participation figures describe a
US shared-resource response. Programme reach is
not proof of equal allocation, global access or
eliminated inequality.
Proposed shared-cluster policy
Publish eligibility, GPU-hour limits and allocation
criteria; reserve some capacity for teaching, smaller
institutions and independent replication.
Provide application support and training; allow
appeals. Track applicant-to-award outcomes and
waiting times across institution groups with privacy
safeguards.
Trade-offs: reservations may reduce immediate
utilization; queueing can delay urgent work;
unrestricted access can conflict with
security/budgets. Prevent repeated deferral or
resource starvation.
Sources: [10] NSF 2026: US programme reach; [11] Strubell et al. 2019: cost and equity; [16] Ahmed and Wahed 2020: compute divide; [22] Topic 9B: mutual exclusion and
allocation
30 / 56
Notes: [10] U.S. National Science Foundation, “NAIRR at 2 years: Advancing American artificial intelligence innovation and leadership,” Mar. 19, 2026, accessed Oct. 8, 2026.
https://www.nsf.gov/cise/updates/nairr-2-years-advancing-american-artificial-intelligence
[11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL, 2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[16] N. Ahmed and M. Wahed, “The de-democratization of AI: Deep learning and the compute divide in artificial intelligence research,” arXiv:2010.15581v1, 2020.
https://arxiv.org/abs/2010.15581v1
[22] Monash University, FIT3143 Topic 9B: Mutual exclusion and resource allocation, course slides, 2024, pp. 4–16, 24–32.
../context/FIT3143-Topic-9B-2024.pdf

## Slide 31
Appendix B7 • Proposed application
Framework roles and accountable decisions
Function / evidence | Concrete action | Decision / responsible role
Govern / OECD values + NIST | Assign ownership, data rules, access policy and escalation | Accountable owner accepts obligations and review process.
Map / NIST | Define use, stakeholders, misuse risks, deadline and alternatives | Data/risk stewards establish the application-specific scope.
Measure / Green AI + NIST | Track energy per useful outcome, model quality, group harms and scaling efficiency | Operator/evaluator provides evidence and uncertainty.
Manage / scheduling research + NIST | Approve, defer, reduce scale or redesign; enforce safeguards and review outcomes | Owner authorizes exceptions or rejects unresolved risks.
Green AI motivates measurement; scheduling research supplies a mechanism; OECD/NIST guide values and risk
management. The combination is our proposal.
Sources: [13] Schwartz et al. 2019: efficiency reporting; [17] Radovanovic et al. 2021: flexible scheduling; [18] OECD: rights, fairness and accountability; [19] NIST: Govern, Map,
Measure, Manage
31 / 56
Notes: [13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 32
Appendix B8 • Illustrative policy
Carbon-aware scheduling under constraints
Flexible job
ready
Lower-carbon
forecast window
Complete before
deadline
Research [17] demonstrates shifting temporally flexible workloads using forecasts while preserving daily
capacity. It does not show every urgent GPU job can wait.
Proposed rule: defer only if deadline, energy budget, water/site limits and equitable waiting-time
commitments remain satisfied; record exceptions.
No feasible window: reduce scale, redesign or approve a justified urgent exception. Prevent indefinite
deferral. Data residency and transfer costs constrain moving work between sites.
Flexible jobs may move; urgent jobs, water constraints and access commitments can override deferral.
Sources: [12] Li et al. 2025 revision: water impacts; [17] Radovanovic et al. 2021: flexible scheduling; [19] NIST: Govern, Map, Measure, Manage
32 / 56
Notes: [12] P. Li, J. Yang, M. A. Islam, and S. Ren, “Making AI less ‘thirsty’: Uncovering and addressing the secret water footprint of AI models,” arXiv:2304.03271v5, Mar. 26, 2025; first submitted 2023.
https://arxiv.org/abs/2304.03271v5
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 33
Appendix B9
Research comparisons across all four topics
Topic | Comparison | Interpretation / limit
(a) Environment | Cost/efficiency research [11,13] versus water-footprint research [12] | Useful-output efficiency and local resource pressure need different measures.
(b) Governance | Gradient reconstruction [14] versus fairness evaluation survey [15] | Data exposure and unequal outcomes are distinct failure mechanisms.
(c) Access | Institutional participation [16] versus workload cost/equity [11] | Concentration and financial barriers reinforce a concern; scopes differ.
(d) Frameworks | Efficiency-reporting argument [13] versus operational scheduling [17] | Measurement motivates action; scheduling depends on flexibility and forecasts.
Current institutional evidence [9,10] and governance frameworks [18,19] complement the research; they do not replace its
methodological limits.
Sources: [11] Strubell et al. 2019: cost and equity; [12] Li et al. 2025 revision: water impacts; [13] Schwartz et al. 2019: efficiency reporting; [14] Zhu et al. 2019: exposed gradients;
[15] Gallegos et al. 2024: fairness evaluation; [16] Ahmed and Wahed 2020: compute divide; [17] Radovanovic et al. 2021: flexible scheduling
33 / 56
Notes: [11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL, 2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[12] P. Li, J. Yang, M. A. Islam, and S. Ren, “Making AI less ‘thirsty’: Uncovering and addressing the secret water footprint of AI models,” arXiv:2304.03271v5, Mar. 26, 2025; first submitted 2023.
https://arxiv.org/abs/2304.03271v5
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597
[14] L. Zhu, Z. Liu, and S. Han, “Deep leakage from gradients,” arXiv:1906.08935v2, 2019.
https://arxiv.org/abs/1906.08935v2
[15] I. O. Gallegos et al., “Bias and fairness in large language models: A survey,” Computational Linguistics, vol. 50, no. 3, pp. 1097–1179, 2024, doi: 10.1162/coli_a_00524.
https://aclanthology.org/2024.cl-3.8/
[16] N. Ahmed and M. Wahed, “The de-democratization of AI: Deep learning and the compute divide in artificial intelligence research,” arXiv:2010.15581v1, 2020.
https://arxiv.org/abs/2010.15581v1
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1

## Slide 34
Appendix • Synthesis
Conclusions and next measurements
GPU rotation
Inverse gathering exposes independent pixel work.
SM scheduling, memory locality and transfer costs
determine achieved performance.
Choose a CPU baseline and compare completed
equivalent pipelines. GDS is conditional on storage
bottlenecks, a compatible data path and verified
support.
Next: compile the teaching examples, check output
against a CPU reference and profile representative
image sizes/angles/batches. No result is assumed.
Responsible scaling
More compute can enable valuable research while
concentrating access and increasing resource
demand. Approve scale for useful outcomes, with
safeguards.
Combine job-level energy/resource evidence,
separate security/fairness evaluation, transparent
allocations and deadline-aware scheduling.
Next: measure a real cluster job’s energy, quality,
scaling efficiency and allocation outcomes; revise
policy when evidence or conditions change.
Sources: [2] Topic 7A: dependencies and Amdahl; [5] NVIDIA CUDA Best Practices; [6] NVIDIA GDS overview; [7] NVIDIA GDS design; [13] Schwartz et al. 2019: efficiency
reporting; [17] Radovanovic et al. 2021: flexible scheduling; [19] NIST: Govern, Map, Measure, Manage
34 / 56
Notes: [2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15, 18–27.
../context/FIT3143-Topic-7A-2024.pdf
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html
[6] NVIDIA, GPUDirect Storage Overview Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/overview-guide/index.html
[7] NVIDIA, GPUDirect Storage Design Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/design-guide/index.html
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/

## Slide 35
Appendix • References 1/6
References
[1] Monash University, FIT3143 Topic 8: Vector processing, GPUs and NPUs, course slides, 2024, pp. 18–23, 32–35,
41–46.
../context/FIT3143-Topic-8-2024.pdf
[2] Monash University, FIT3143 Topic 7A: Parallel performance and Amdahl reasoning, course slides, 2024, pp. 6–15,
18–27.
../context/FIT3143-Topic-7A-2024.pdf
[3] Monash University, FIT3143 Topic 9A: Synchronization and dependencies, course slides, 2024, pp. 2–7.
../context/FIT3143-Topic-9A-2024.pdf
[4] NVIDIA, “Programming model,” CUDA Programming Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-programming-guide/01-introduction/programming-model.html
FIT3143 Applied 2
35 / 56

## Slide 36
Appendix • References 2/6
References
[5] NVIDIA, CUDA C++ Best Practices Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html
[6] NVIDIA, GPUDirect Storage Overview Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/overview-guide/index.html
[7] NVIDIA, GPUDirect Storage Design Guide, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/gpudirect-storage/design-guide/index.html
[8] NVIDIA, “Parallelism strategies guide,” Megatron Core, online documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/megatron-core/developer-guide/latest/user-guide/parallelism-guide.html
FIT3143 Applied 2
36 / 56

## Slide 37
Appendix • References 3/6
References
[9] International Energy Agency, Key Questions on Energy and AI, executive summary, Apr. 16, 2026, CC BY 4.0, accessed
Oct. 8, 2026.
https://www.iea.org/reports/key-questions-on-energy-and-ai/executive-summary
[10] U.S. National Science Foundation, “NAIRR at 2 years: Advancing American artificial intelligence innovation and
leadership,” Mar. 19, 2026, accessed Oct. 8, 2026.
https://www.nsf.gov/cise/updates/nairr-2-years-advancing-american-artificial-intelligence
[11] E. Strubell, A. Ganesh, and A. McCallum, “Energy and policy considerations for deep learning in NLP,” in Proc. ACL,
2019, pp. 3645–3650, doi: 10.18653/v1/P19-1355.
https://aclanthology.org/P19-1355/
[12] P. Li, J. Yang, M. A. Islam, and S. Ren, “Making AI less ‘thirsty’: Uncovering and addressing the secret water footprint of
AI models,” arXiv:2304.03271v5, Mar. 26, 2025; first submitted 2023.
https://arxiv.org/abs/2304.03271v5
FIT3143 Applied 2
37 / 56

## Slide 38
Appendix • References 4/6
References
[13] R. Schwartz, J. Dodge, N. A. Smith, and O. Etzioni, “Green AI,” arXiv:1907.10597, 2019.
https://arxiv.org/abs/1907.10597
[14] L. Zhu, Z. Liu, and S. Han, “Deep leakage from gradients,” arXiv:1906.08935v2, 2019.
https://arxiv.org/abs/1906.08935v2
[15] I. O. Gallegos et al., “Bias and fairness in large language models: A survey,” Computational Linguistics, vol. 50, no. 3,
pp. 1097–1179, 2024, doi: 10.1162/coli_a_00524.
https://aclanthology.org/2024.cl-3.8/
[16] N. Ahmed and M. Wahed, “The de-democratization of AI: Deep learning and the compute divide in artificial intelligence
research,” arXiv:2010.15581v1, 2020.
https://arxiv.org/abs/2010.15581v1
FIT3143 Applied 2
38 / 56

## Slide 39
Appendix • References 5/6
References
[17] A. Radovanovic et al., “Carbon-aware computing for datacenters,” arXiv:2106.11750v1, 2021.
https://arxiv.org/abs/2106.11750v1
[18] OECD, “OECD AI Principles,” adopted 2019, updated 2024, accessed Oct. 8, 2026.
https://www.oecd.org/en/topics/ai-principles.html
[19] NIST, AI Risk Management Framework 1.0 Playbook, framework 2023, current online resource, accessed Oct. 8, 2026.
https://airc.nist.gov/airmf-resources/playbook/
[20] NVIDIA, “Rotate,” NPP Image Geometry Transforms, CUDA 13.0.3 archive documentation, accessed Oct. 8, 2026.
https://docs.nvidia.com/cuda/archive/13.0.3/npp/image_geometry_transforms.html#rotate
FIT3143 Applied 2
39 / 56

## Slide 40
Appendix • References 6/6
References
[21] Monash University, FIT3143 Week 5 combined course material, MPI collectives, pp. 148–155.
../context/FIT3143_Week_5_Combined.pdf
[22] Monash University, FIT3143 Topic 9B: Mutual exclusion and resource allocation, course slides, 2024, pp. 4–16, 24–32.
../context/FIT3143-Topic-9B-2024.pdf
FIT3143 Applied 2
40 / 56

## Slide 41
Appendix • AI declaration
AI assistance and prompt-record provenance
Tools and assistance
OpenAI Codex was used on 6 and 8 October 2026
for research/source checks, drafting and revision,
CUDA teaching examples, editable slide
diagrams/charts and presentation assembly.
AI supported preparation. Students must understand
and validate submitted work; no AI use is permitted
during presentation/interview.
Charts are cited sector evidence. Worked examples
and policy scenarios are labeled illustrative; CUDA
performance was not measured.
Record included in this deck
Earlier preparation prompts are reproduced from the
saved Task 1 and Task 2 records with original
spelling. The continuation records the available 8
October requests and supplied details.
A recorded review goal is labeled as such, separate
from direct user prompts. Environment/system
instructions and assistant/tool output are not
presented as student prompts.
The accompanying PDF contains this same
presentation, including these records. Any
subsequent AI preparation must be appended
before submission.
FIT3143 Applied 2
41 / 56

## Slide 42
Appendix • 6 October 2026 • Prompt record 1
Earlier task1 preparation, record 1
# AGENTS.md instructions
<INSTRUCTIONS>
"You are an expert computer science professor and senior software engineer acting as a student mentor.Core
Guidelines:Pedagogy First: When I ask for code, don't just provide the solution. Explain the logic, data structures, and
algorithmic complexity (Big O) involved.Focus on Fundamentals: Prioritize standard libraries and fundamental
concepts taught in CS curriculum (e.g., Data Structures & Algorithms, Operating Systems).Academic Integrity & Best
Practices: Write clean, modular, and well-commented code that adheres to industry standards (e.g., PEP8 for
Python).Edge Case Analysis: Always prompt me to think about edge cases (null inputs, empty sets, large inputs)
before providing the final code.Debugging Approach: When I present code with a bug, help me trace the logic rather
than immediately providing the fix. Ask probing questions to guide me to the answer."
</INSTRUCTIONS>
FIT3143 Applied 2
42 / 56

## Slide 43
Appendix • 6 October 2026 • Prompt record 2
Earlier task1 preparation, record 2
in folder "Applied 2" you will have the content I want you to work on, explain me what i need to do for task 1(since task
2 is done by someboday else), create evrrythign later on if your creating in this folder, you can access all the content
in this folder and help me do this applied correctly, fo rthe moment only tell me what I need to do for task 1
FIT3143 Applied 2
43 / 56

## Slide 44
Appendix • 6 October 2026 • Prompt record 3 (1/3)
Earlier task1 preparation, record 3
here is some more context as well which you can add on - Parallel Computer Applied 10 - Based on image rotations
Include diagrams
for task 1 - (4min)
focus on the Part D of the workshop from collab -
Part D: Reflection Questions
Answer the following questions.
What is the role of the host and device in CUDA?
How are threads organised into blocks and grids?
Why is brightness adjustment considered a data-parallel problem?
Why does GPU acceleration generally improve as image size increases?
What overhead is introduced by CPU-GPU memory transfers?
FIT3143 Applied 2
44 / 56

## Slide 45
Appendix • 6 October 2026 • Prompt record 3 (2/3)
Earlier task1 preparation, record 3
How many threads are launched when using:
Image = 1024 x 1024
Block Size = 16 x 16
If the GPU contained thousands of CUDA cores, how can they process millions of image pixels?
Task 2 - (3min)
explain how HPC is related to parallel computing
how HPC relates to scaling and AI
make sure to include statistics adn charts(make sure to get proper citation) and make sure you are able to properly
explain this and the trend.
- make sure to cover a few points not all (out of a,b,c,d), but not all have to be in detail (since some of them overlap) -
make sure atleast 1 point is explained in detail.
FIT3143 Applied 2
45 / 56

## Slide 46
Appendix • 6 October 2026 • Prompt record 3 (3/3)
Earlier task1 preparation, record 3
Ex:
total time to present 7 mins
can task 1 be done by you or does it reqrueis desgnig somethign ? if you can do it go ahead and do task 1
FIT3143 Applied 2
46 / 56

## Slide 47
Appendix • 6 October 2026 • Prompt record 4
Earlier task2 preparation, record 1
Are you able to push the changes to this git page and create a new folder named applied2
https://github.com/Shamle-T/FIT3143-Parallel-Computing dont include any refernces of codex in the naming when
your creating a new folder. Let me know whether this is possible
FIT3143 Applied 2
47 / 56

## Slide 48
Appendix • 6 October 2026 • Prompt record 5
Earlier task2 preparation, record 2
using a detailed comit message push the current changes to git and also do we need to do any code for task 1?
once pushed do task 2 as well, and push the task 2 to git are required
FIT3143 Applied 2
48 / 56

## Slide 49
Appendix • 6 October 2026 • Prompt record 6
Earlier task2 preparation, record 3
1)once you have compelted task 2, make sure you have aimed for HD in rubric yeah? for both task 1 and task 2 - if
not update both tasks to cover HD level in the rubric
2) create a 6 minute script for both me (task1) and (task2) for my firend , make sure it doesnt sound overly robotic
since we will have to speak this out.
FIT3143 Applied 2
49 / 56

## Slide 50
Appendix • 6 October 2026 • Prompt record 7
Earlier task2 preparation, record 4
Six minutes total: 3 minutes each
FIT3143 Applied 2
50 / 56

## Slide 51
Appendix • 8 October 2026 • Prompt record 8
Repository synchronization
pull the latest from the remote repo, push any local changes and merge, local changes arent important. main goal is
to get the latest version of the "applied2" dir from the remote
FIT3143 Applied 2
51 / 56

## Slide 52
Appendix • 8 October 2026 • Prompt record 9
Review request
- review the content in the root level context folder (with an emphasis on week's 7-9).
- Review the solutions to task 1 and task 2 in [applied2](applied2/) based on the specification [Applied #2 -
Assessment Specification.pdf](<\<applied2/assessment/Applied #2 - Assessment Specification.pdf\>>) . Identify any
key HD blockers in the solutions based on the rubric attached.
- The solutions dont need to only use the theory in the context folder but where possible, they should.
FIT3143 Applied 2
52 / 56

## Slide 53
Appendix • 8 October 2026 • Prompt record 10
Current preparation instructions
# AGENTS.md instructions
<INSTRUCTIONS>
- Answer immediately without intro pleasantries, prompt repetitions, or polite filler.
- Be concise. Avoid conversational fluff, over-explanation, and unsolicited summaries.
- Rely strictly on verified facts. Never invent URLs, names, statistics, or quotes.
- If an answer cannot be verified with absolute certainty, state "I do not know" instead of guessing.
- For complex logic, perform brief step-by-step reasoning before delivering the final answer.
</INSTRUCTIONS>
FIT3143 Applied 2
53 / 56

## Slide 54
Appendix • 8 October 2026 • Recorded goal 11
Recorded review goal
Review the solutions to task 1 and task 2 in [applied2](applied2/) based on the specification [Applied #2 - Assessment
Specification.pdf](<applied2/assessment/Applied #2 - Assessment Specification.pdf>) . Identify any key HD blockers
in the solutions based on the rubric attached. Dont stop until you are certain you have identified every HD blocker and
created an action plan which you can later execute to update the solutions to fix all problems.
FIT3143 Applied 2
54 / 56

## Slide 55
Appendix • 8 October 2026 • Prompt record 12
Revision and presentation request
Now, fix all the identified problems and HD blockers. Don't stop until you're confident that task 1 and task 2 have a
high probability of achieving an HD as per the applied-to rubric. Also refer to teaching_team_guidance.md, which is in
the applied2 directory. Also ignore the Q&A and "Presentation Quality" in the rubric as these will be done by me. You
need to create the presentation but dont worry about presenting it. Once you are confident with the task 1 and 2
solutions create a presentation as per task 3 (again dont worry about task 3 part c). Ensure the presentation is
professionally formatted and contains all key details as I will not be submitting any other report, all info must be
present in the presentation.
FIT3143 Applied 2
55 / 56

## Slide 56
Appendix • 8 October 2026 • Prompt record 13
Identification details supplied
Savin Vindiv De Alwis (35221631) - sdea0018@student.monash.edu
Shamle Thilaksiri (35512075) - wthi0003@student.monash.edu
FIT3143 Applied 2
56 / 56