## Slide 1
BASE STATION
FIT3143 • APPLIED #1
Distributed Wireless
Sensor Network
Electric Vehicle Charging Navigation System Simulation
A hybrid MPI + OpenMP architecture over a 2-D mesh topology
Savin Vindiv De Alwis • 35221631
Shamle Thilaksiri • 35512075
Week 6 Assessment

## Slide 2
DESIGN OVERVIEW
System at a glance
The report converges on four decisions that define the simulator and its communication behaviour.
TASK 1
2-D mesh topology
Orthogonal north / south / east / west neighbours model immediate geographic adjacency.
TASK 2
Hybrid MIMD
MPI ranks model distributed EV charging stations; OpenMP threads parallelise work within each station.
TASK 2
Non-blocking MPI
Neighbour queries and replies use MPI_Isend / MPI_Irecv with local MPI_Waitall synchronization.
TASK 3
Scalable traffic model
One fixed message stays O(1); aggregate traffic grows O(N), while S base stations reduce peak load toward O(N/S).
d ≤ 4
MAXIMUM MESH NODE DEGREE
N + 1
MPI PROCESSES
1 Gbit/s
ANALYTICAL LINK BANDWIDTH
< 1%
MODELLED LOAD AT N=256, 20 HZ

## Slide 3
TASK 1 • NETWORK TOPOLOGY
Why the 2-D mesh wins
The selected topology trades absolute minimum diameter for geographic realism, bounded fan-out and O(N) link cost.
ASSESSMENT PRIORITIES
Immediate adjacency
Stations communicate with physically adjacent nodes.
2-D geography
The network represents a Cartesian area, not an abstract logical cube.
Low local fan-out
Corner / edge / interior degree is 2 / 3 / 4.
Scalable link cost
Prefer O(N) rather than O(N²) physical connectivity.
Topology
Geographic realism
Neighbour fit
Link cost
Decision
2-D mesh
Excellent
Direct
O(N)
SELECT
2-D torus
Moderate
Direct
O(N)
CONSIDER
Hypercube
Poor
Logical
O(N log N)
REJECT
Complete
Poor
Every node
O(N²)
REJECT
Decision: 2-D mesh is the closest match to the specification because neighbour relationships are native to the topology — not imposed through a hub or abstract logical mapping.

## Slide 4
TASK 1 • SELECTED TOPOLOGY
Selected logical WSN: 3 × 3 mesh
Solid links represent immediate orthogonal neighbours. Dashed links represent direct logical MPI communication with the base station.
EVCS 1
EVCS 2
EVCS 3
EVCS 4
EVCS 5
EVCS 6
EVCS 7
EVCS 8
EVCS 9
BASE
STATION
MPI rank 0
WHY IT FITS
≤ 4
NODE DEGREE
O(N)
LINK COST
O(√N)
DIAMETER
√N
BISECTION
Nearest-node redirection uses Manhattan distance:
d = |rₛ − rⱼ| + |cₛ − cⱼ|
This matches the minimum number of orthogonal grid steps.

## Slide 5
TASK 2 • DEPLOYMENT
Hybrid MIMD architecture
MPI maps distributed components across machines; OpenMP parallelises work inside each EVCS process.
10
MPI RANKS
37
PHYSICAL CORES
3
16-CORE MACHINES
4
OPENMP THREADS / EVCS
1 Gbit/s
INTER-MACHINE LINK
MACHINE 1
13 cores used
BASE • rank 0
EVCS 1 • rank 1
OpenMP ×4
EVCS 2 • rank 2
OpenMP ×4
EVCS 3 • rank 3
OpenMP ×4
MACHINE 2
12 cores used
EVCS 4 • rank 4
OpenMP ×4
EVCS 5 • rank 5
OpenMP ×4
EVCS 6 • rank 6
OpenMP ×4
MACHINE 3
12 cores used
EVCS 7 • rank 7
OpenMP ×4
EVCS 8 • rank 8
OpenMP ×4
EVCS 9 • rank 9
OpenMP ×4
CLUSTER
INTERCONNECT
MPI
distributed-memory
message passing
1 Gbit/s
baseline
Logical WSN coordinates remain independent of physical MPI rank placement.

## Slide 6
TASK 2 • STATIC MODEL
Software structure and message protocol
Each MPI process owns its local state. Shared memory exists only inside an EVCS process; cross-process state moves through explicit messages.
CORE COMPONENTS
BaseStation
MPI rank 0
Status table • congestion alerts • nearest available node • redirect command
EVChargingNode
MPI ranks 1…N
Coordinates • threshold • neighbour ranks • local ports • status / query / alert logic
ChargingPort
Shared-memory object
Free / occupied state; OpenMP partitions port work.
NodeStatus
Compact record
node ID • row • column • free/total ports • utilisation
MPI messages
owns 1…P
produces
MESSAGE TAGS
STATUS_UPDATE
EVCS → base
28 B
NEIGHBOUR_QUERY
EVCS → adjacent EVCS
8 B
NEIGHBOUR_REPLY
adjacent EVCS → requester
20 B
CONGESTION_ALERT
EVCS → base
32 B
REDIRECT_COMMAND
base → EVCS
16 B
NodeStatus can be sent as one logical message using an MPI derived datatype or packed representation.

## Slide 7
TASK 2 • MESSAGE PASSING
Simulation workflow: local work, local synchronization
The critical design choice is to avoid a global barrier: each node waits only for the neighbour information required for its own decision.
01
Update local ports
OpenMP parallel-for
02
Aggregate utilisation
OpenMP reduction
03
Send NodeStatus
MPI_Isend → rank 0
04
Threshold check
utilisation > threshold?
YES
Post neighbour receives
MPI_Irecv first
Issue neighbour queries
MPI_Isend to valid mesh neighbours
Wait for required replies
MPI_Waitall — local synchronization
All neighbours congested?
If yes → CONGESTION_ALERT
Base station selects closest available EVCS and sends REDIRECT_COMMAND
NO GLOBAL MPI_BARRIER
Fast ranks do not wait for the slowest rank; message passing provides both data movement and the synchronization needed by the decision.

## Slide 8
TASK 2 • SIZING
Resource mapping and base-station selection
The simulator scales by MPI process count across stations and by OpenMP thread count inside each charging node.
N + 1
MPI processes
N charging nodes + one base station
NT + 1
Physical-core demand
T OpenMP threads per EVCS + rank 0
⌈(NT + 1) / C⌉
Machines required
C usable physical cores per machine
3 × 3 WORKED EXAMPLE
N = 9 • T = 4 • C = 16
10 MPI ranks → 37 cores → 3 machines
BASE-STATION REDIRECTION ALGORITHM
1
Filter
Keep candidates with a free port and utilisation ≤ threshold.
2
Measure
Compute Manhattan distance from alerting source to each candidate.
3
Select
Choose minimum distance; break ties by lowest MPI rank.
4
Redirect
Send target node ID and coordinates back to the alerting EVCS.
Baseline search cost: O(N) per congestion alert.
THREADING RULE
T = min(P, Tₘₐₓ)
Do not create one thread per charging port. Bind cores to prevent OpenMP oversubscription.

## Slide 9
TASK 3 • ANALYTICAL MODEL
Communication model: fixed messages stay O(1)
For the baseline, each message is one logical hop over a 1 Gbit/s link. Queueing, processing and propagation delay are intentionally excluded.
STORE-AND-FORWARD MODEL
Tₜₓ = (L × H) / B
L = message length (bits)
H = hop count = 1
B = 10⁹ bit/s
KEY INTERPRETATION
Increasing N does not change a fixed message’s bit length.
Per-message transmission time remains O(1); N increases how many messages are exchanged.
ONE-HOP PAYLOAD TRANSMISSION TIME
CONGESTION_ALERT
0.256 μs
32 B
STATUS_UPDATE
0.224 μs
28 B
NEIGHBOUR_REPLY
0.160 μs
20 B
REDIRECT_COMMAND
0.128 μs
16 B
NEIGHBOUR_QUERY
0.064 μs
8 B
All five curves would be flat versus N because L, H and B are fixed.

## Slide 10
TASK 3 • N SCALING
Scaling with charging nodes: aggregate demand grows O(N)
The mesh keeps local degree bounded, but more active MPI ranks increase the number of status, query/reply and alert/redirect messages per simulation round.
Chart: 
| 4 | 16 | 36 | 64 | 100 | 144 | 196 | 256 | 400 | 576 | 784 | 1024
STATUS_UPDATE | 0.896 | 3.584 | 8.064 | 14.336 | 22.4 | 32.256 | 43.904 | 57.344 | 89.6 | 129.024 | 175.616 | 229.376
NEIGHBOUR_QUERY | 0.512 | 3.072 | 7.68 | 14.336 | 23.04 | 33.792 | 46.592 | 61.44 | 97.28 | 141.312 | 193.536 | 253.952
NEIGHBOUR_REPLY | 1.28 | 7.68 | 19.2 | 35.84 | 57.6 | 84.48 | 116.48 | 153.6 | 243.2 | 353.28 | 483.84 | 634.88
CONGESTION_ALERT | 1.024 | 4.096 | 9.216 | 16.384 | 25.6 | 36.864 | 50.176 | 65.536 | 102.4 | 147.456 | 200.704 | 262.144
REDIRECT_COMMAND | 0.512 | 2.048 | 4.608 | 8.192 | 12.8 | 18.432 | 25.088 | 32.768 | 51.2 | 73.728 | 100.352 | 131.072
WHAT SCALES
O(1)
ONE MESSAGE
O(N)
TOTAL TRAFFIC
Square mesh
E = 2(N − √N)
Directed query/reply relationships
4(N − √N)
Main fan-in point
A single base station receives O(N) status / alert traffic per interval.

## Slide 11
TASK 3 • S SCALING
Adding base stations distributes the fan-in load
With N = 256 and balanced assignment, base-station-bound service demand falls approximately as 1/S. Neighbour traffic does not change.
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
STATUS_UPDATE | 57.344 | 28.672 | 19.1147 | 14.336 | 11.4688 | 9.5573 | 8.192 | 7.168 | 6.3716 | 5.7344 | 5.2131 | 4.7787 | 4.4111 | 4.096 | 3.8229 | 3.584
CONGESTION_ALERT | 65.536 | 32.768 | 21.8453 | 16.384 | 13.1072 | 10.9227 | 9.3623 | 8.192 | 7.2818 | 6.5536 | 5.9578 | 5.4613 | 5.0412 | 4.6811 | 4.3691 | 4.096
REDIRECT_COMMAND | 32.768 | 16.384 | 10.9227 | 8.192 | 6.5536 | 5.4613 | 4.6811 | 4.096 | 3.6409 | 3.2768 | 2.9789 | 2.7307 | 2.5206 | 2.3406 | 2.1845 | 2.048
NEIGHBOUR_QUERY | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256 | 0.256
NEIGHBOUR_REPLY | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64 | 0.64
SCALING RESULT
O(N/S)
peak base-station load
STATUS_UPDATE, CONGESTION_ALERT and REDIRECT_COMMAND fall as S grows.
NEIGHBOUR_QUERY / REPLY remain constant because EVCS degree stays ≤ 4.
Real systems may gain further from reduced queueing, but base-station coordination adds overhead.

## Slide 12
TASK 3 • SENSITIVITY ANALYSIS
Reporting frequency scales bandwidth linearly
For N = 256 under the report’s worst-case message mix, payload bandwidth is O(f) and remains far below the 1 Gbit/s analytical link capacity.
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Total worst-case WSN payload | 0.37069 | 0.74138 | 1.1121 | 1.4828 | 1.8534 | 2.2241 | 2.5948 | 2.9655 | 3.3362 | 3.7069 | 4.0776 | 4.4483 | 4.8189 | 5.1896 | 5.5603 | 5.931 | 6.3017 | 6.6724 | 7.0431 | 7.4138
Base-station-bound payload | 0.15565 | 0.3113 | 0.46694 | 0.62259 | 0.77824 | 0.93389 | 1.0895 | 1.2452 | 1.4008 | 1.5565 | 1.7121 | 1.8678 | 2.0234 | 2.1791 | 2.3347 | 2.4904 | 2.646 | 2.8017 | 2.9573 | 3.113
AT N = 256
46,336 B
WORST-CASE PAYLOAD / ROUND
0.371 Mbit/s
at 1 Hz
3.707 Mbit/s
at 10 Hz
7.414 Mbit/s
at 20 Hz • < 1% of 1 Gbit/s
Headers, wireless interference, simultaneous-flow queueing and MPI protocol effects can raise observed latency beyond this payload-only model.

## Slide 13
CONCLUSION
What the analysis supports
The proposed architecture is communication-light under the baseline model, while preserving a clear path to scale the base-station layer and improve realism.
2-D mesh
Best fit for immediate geographic neighbours
Hybrid MIMD
MPI across processes • OpenMP inside EVCS
O(N)
Aggregate communication as the WSN grows
O(N/S)
Peak base-station load with S balanced servers
BASELINE LIMITATIONS
Excludes wireless interference, packet loss, propagation, queueing, MPI headers and OS scheduling.
Base station is a direct MPI endpoint rather than a multi-hop wireless destination.
Manhattan distance approximates proximity; real road / GPS distance is not modelled.
FUTURE WORK
Regional base stations with synchronized status replication.
Failure-aware and multi-hop routing over the wireless mesh.
Measured MPI latency / throughput and dynamic vehicle arrival workloads.
GPS / road-network distance for practical redirection.
Bottom line: fixed-size messages remain cheap; the primary scalability pressure is aggregate fan-in at the base station, not neighbour communication.

## Slide 14
Q&A REFERENCE
Appendix: topology comparison
Static network parameters reproduced from the report’s Week 5 comparison, with the selected mesh highlighted.
Topology | Degree | Diameter | Bisection | Arc conn. | Cost
Linear array | 1–2 | N−1 | 1 | 1 | N−1
Ring | 2 | N/2 | 2 | 2 | N
Star | 1 or N−1 | 2 | 1 | 1 | N−1
Binary tree | 1–3 | 2 log₂((N+1)/2) | 1 | 1 | N−1
2-D mesh | 2–4 | 2(√N−1) | √N | 2 | 2(N−√N)
2-D torus | 4 | √N | 2√N | 4 | 2N
3-D cube | 3–6 | 3(∛N−1) | N^(2/3) | 3 | 3(N−N^(2/3))
Hypercube | log₂N | log₂N | N/2 | log₂N | N log₂N / 2
Complete | N−1 | 1 | N²/4 | N−1 | N(N−1)/2

## Slide 15
Q&A REFERENCE
Appendix: message protocol and complexity
Message sizes are payload-only: 4-byte int and 8-byte double fields; MPI / transport headers and padding are excluded.
Tag | Direction | Bytes | MPI behaviour | Complexity
STATUS_UPDATE | EVCS → base | 28 | MPI_Isend; async receive at base | O(1) / msg
NEIGHBOUR_QUERY | EVCS → neighbour | 8 | MPI_Isend after posting replies | O(1) / msg
NEIGHBOUR_REPLY | Neighbour → requester | 20 | MPI_Isend / Irecv + Waitall | O(1) / msg
CONGESTION_ALERT | EVCS → base | 32 | MPI_Isend; event-driven | O(1) / msg
REDIRECT_COMMAND | Base → EVCS | 16 | Point-to-point response | O(1) / msg
Synchronization rule
Post reply receives first → issue non-blocking queries → wait only for required neighbour replies. This avoids circular blocking and removes the need for a global barrier.

## Slide 16
APPENDIX
References and AI declaration
The presentation is condensed from the submitted report and preserves its references and declared assumptions.
REFERENCES
[1] Monash University, FIT3143 Applied #1 Assessment (Week 6): Distributed Wireless Sensor Network, 2026.
[2] Monash University, FIT3143 Applied #1 Marking Rubric (Week 6), 2026.
[3] FIT3143 Topic 5: Multiple Instruction Multiple Data and Distributed Memory Architectures, 2024.
[4] FIT3143 Week 5 Applied Preparation / MPI material, 2024.
[5] FIT3143 Week 3 Lab Preparation: OpenMP shared-memory data environment, work sharing and reduction, 2024.
[6] FIT3143 Topic 1: Introduction to Parallel Computing, 2024.
[7] Consolidated MPI examples supplied with the unit / project sources.
AI DECLARATION
Declared tool
ChatGPT (OpenAI)
Purpose
Preparation, analysis support, editing, diagram / graph generation and formatting.
Responsibility
Authors remain responsible for validating technical accuracy and explaining the work independently during presentation and Q&A.